## Slide 1: System Identification to support Flight Test activities
22.01.2018
Alejandro Valverde

## Slide 2: Problems in Aircraft Dynamics
@ Kopter Group AG | Alejandro Valverde
Input, u
System, S
Output, z
Simulation: Given u and S, find z
Control: Given z and S, find u
Identification: Given z and u, find S

## Slide 3: Motivations to the use System ID techniques
Verify and validate theoretical predictions for rotorcraft behaviour
Validate linearization of full helicopter dynamics from FlightLab and help development of FCS
Implement a FCS into FlightLab
Expansion of flight envelope for new aircraft
@ Kopter Group AG | Alejandro Valverde

## Slide 4: Applied to simulation
@ Kopter Group AG | Alejandro Valverde
System ID provides an accurate, simple and reliable model of the H/C dynamics obtained from real flight test data of the real H/C
Extracted from Nicolas’ MSc Thesis overview in collaboration with Kopter Avionics Dep.
LUTs
Equations of Motion
Dynamic Simulation
Aerodynamic H/C model
Pilot inputs
Notes: Accurate -> Because it’s based on real flight data
Simple -> Does not require high computational power
Reliable -> Computed with

## Slide 5: How does it work?
@ Kopter Group AG | Alejandro Valverde
Forces and moments
Develop a model form from which parameters can be estimated using flight test data
for example,
for the pitching moment coef.
static stability
dynamic stability (damping)
pitch control authority
pitching moment bias
H/C angle of attack
longitudinal angular velocity
pitch control input

## Slide 6: How does it work?
@ Kopter Group AG | Alejandro Valverde

## Slide 7: Tools
@ Kopter Group AG | Alejandro Valverde
Already available
No development time needed
Proven industry suitable software
Further ways:
    Python implementation

## Slide 10: Why to introducing System ID into P3 test campaign?
To boost flight test productivity
Structure issues problems seem to be solved with P3, time to assess the handling qualities
Surely it will be need for PS4 and further developments after TC
Every big H/C DOA does it
System ID takes time and money – but not nearly as much as not doing it
@ Kopter Group AG | Alejandro Valverde

## Slide 11: What would I need?
A laptop
some accelerometers installed in P3, a part from the usual instrumentation…
Some coffee
@ Kopter Group AG | Alejandro Valverde

## Slide 12: Why I can be the one doing this?
Dilemma, won’t hide it
Inexperience industrial <-> Passion
(but yes with System ID)
Kopter experience
Data analysis experience
        Python
        Matlab
        Data analysis and machine learning techniques
@ Kopter Group AG | Alejandro Valverde

## Slide 13
@ Kopter Group AG | Alejandro Valverde

## Slide 14: Thank you